## Slide 1: A Statistical Analysis of UA WiFi Network Speed
STAT 571B – May 1, 2017
Cameron Dorsett, Goutham Gunanjipalli, Kensaku Okada
Notes: Cameron

## Slide 2: Background & Introduction
The Experiment:
  Does UA WiFi Network Speed change with respect to location, time, day of the week, and device?
Meetings with University Information Technology Services (UITS)
  Understanding of UA WiFi Network Structure
Data Collection
  iPerf- network bandwidth measurement tool
Notes: Cameron

## Slide 3: An Overview: UA WiFi Network Infrastructure
Network Core: 3 Cisco routers/servers
  Access to the internet for U of A
Distribution routers
  Backup/secure the network core in case of connection failure
Switches
  Connect individual devices to routers and internet
Access Points (APs)
  Connect to switches
  Allow devices to access wirelessly
  9400 around campus
IEEE 802.11 WiFi standards
  Specific to device and AP
  802.11AC – Shantz & Forbes
    A, B, G, N, AC, etc.
Notes: Goutham

## Slide 4: Design of Experiment
Factorial Design
  24 Total Combinations of Treatments
Treatment Factors
  1st Treatment- Location, 3 levels: Forbes Basement, Shantz 440, Main Library
  2nd Treatment- Day, 2 levels: Sunday & Friday
  3rd Treatment- Time, 2 levels: 9 am & 4 pm
  4th Treatment- Who’s PC?, 2 levels: Goutham & Cameron
40 replications/treatment (10 reps/reading * 4 readings/treatment)
  Observing network speed (bandwidth) @ units of [Mbits/s] via iPerf
Notes: Goutham

## Slide 5: Methodology: iPerf
Simulates Client/Server interaction
  Kensaku: Server
  Goutham & Cameron: Client
Provides network bandwidth readings
  [Mbit/s]
Data collection according to design
Notes: Goutham

## Slide 6: Methodology: SAS
Full Factorial Design chosen to study interactions between all treatment factors
Nuisance factors eliminated through iPerf and design of experiment
  Ex(s): distance from APs, location of server, network path
Response variable: network speed [Mbits/s]
Notes: Goutham

## Slide 7: ANOVA & P-value Tables
Notes: Cameron

## Slide 8: SAS Results
Based on the plot we can infer:
  Main library had slowest network speed on Sunday evening
  Outlier:
    Sunday morning
    Shantz 440
    Cameron’s PC
Average network speed: 111.3 [Mbits/s]
Notes: Cameron

## Slide 9
Notes: Cameron/Goutham

## Slide 10: Conclusions & Recommendations
All interactions of treatment factors statistically significant except for Time
Among 3 Locations:
  Shantz slowest speed
  Forbes basement slightly greater than Main Library
Time with little influence on speed; same can be said for Day
Who’s PC? – PC had greater influence on network speed
  Ex(s): processing speed, WiFi module, etc.
Notes: etc

## Slide 11: Questions & References
Questions?
Special thanks to Dr. An, UITS team, and Brian Little
Notes: etc